## Slide 1: Dispersion and Exchanges

## Slide 3: Diffusion and Dispersion
Diffusion: process where a constituent moves from a higher concentration to a lower concentration
Dispersion: mixing caused by physical processes
time

## Slide 4: Diffusion and Dispersion
Molecular Diffusion: Random motion of particles
Eddy Diffusion: Turbulent mixing of particles
Mechanical Dispersion: mixing caused by variations in velocities

## Slide 5: Mathematical Representations
Diffusion:
  Fick’s First Law of Diffusion
    Flux =
Dispersion:
  Analogous to Fick’s First Law
C1
C2
L12
Exchange =

## Slide 6: Range of Values for Diffusion and Dispersion
Process | Direction | Typical Range [m2/s]
Molecular Diffusion | Vertical | 10-8 to 10-9
 | Lateral | 10-8 to 10-9
 | Longitudinal | 10-8 to 10-9
Turbulent Diffusion | Vertical | 10-6 to 10-2
 | Lateral | 10-2 to 102
 | Longitudinal | 10-2 to 102
Dispersion | Vertical | 10-3 to 10-1
 | Lateral | 10-2 to 100
 | Longitudinal | 10-1 to 104

## Slide 7: Diffusion Coefficients
Condition | Dispersion Coefficient [m2/s]
Molecular Diffusion | 10-9
Compacted Sediment | 10-11 to 10-9
Bioturbated Sediment | 10-9 to 10-8
Lakes – Vertically | 10-6 to 10-4
Large Rivers – Lateral | 10-4 to 10-3
Large Rivers – Longitudinal | 100 to 102
Estuaries – Longitudinal | 102 to 103
From Schnoor, Environmental Modeling: Fate and Transport of Pollutants in Water, Air, and Soil, 1996.

## Slide 8: Determining Dispersion
Streams & Rivers
  Generally Neglect Dispersion
  Determine by Calibration or Dye Study
Estuaries
  Calibration to Salinity data using observed downstream boundary concentration as the forcing function
Lakes
  Calibration to Temperature Data
  Calibration to Chloride Data

## Slide 9: Dispersion in Rivers
Longitudinal Dispersion Coefficient in Rivers, Ex [m2/sec]
= Mean Velocity [m/sec]
B = Width, [m]
d = Depth (hydraulic radius), [m]
u* = Shear Velocity, [m/sec]
=
S = Channel Slope [m/m]
Fischer, et al., 1979.

## Slide 10: Dispersion in Rivers
Lateral Dispersion Coefficient in Rivers, Ey [m2/sec]
d = Depth (hydraulic radius), [m]
u* = Shear Velocity, [m/sec]
 = 0.23 (long, wide lab flume) Elder, 1959
= 0.17 (straight lab flume)
Sayre (1973), Sayre and Chang (1968)
= 0.22 – 0.65, most 0.3
Yotsukura and Cobb(1972), Yotsukura and Sayre (1976)
Elder, 1959.
Ey = du*

## Slide 11: Dispersion in Rivers
Vertical Dispersion Coefficient in Rivers, Ez [m2/sec]
K = von Karman coefficient, ~ 0.4
d = Depth (hydraulic radius), [m]
u* = Shear Velocity, [m/sec]
Jobson and Sayre, 1970.

## Slide 12: Dispersion in Lakes
Vertical Dispersion Coefficient in Lakes, Ez [m2/sec]
d = Depth, [m]
Jobson and Sayre, 1970.

## Slide 13: Dispersion Measurements
Chattahoochee River, GA | Ex = 32.5 m2/s
Susquehanna River, PA | Ex = 92.9 m2/s
Missouri River, NB-IA | Ex = 465 – 1487 m2/s
Antietam Creek, MD | Ex = 9.3 - 25.6 m2/s
Powell River, TN | Ex = 9.5 m2/s
Lake Onondaga, NY | Ez = 0.005 – 0.09 cm2/s (across thermocline)
Lake Zurich, Switzerland | Ez = 0.02 – 0.71 cm2/s (across thermocline)
Lake Erie | Ez = 0.21 cm2/s (across thermocline)
Lake Ontario | Ez = 0.063 – 0.0125 cm2/s (across thermocline)
Lake Erie | Ez = 15 cm2/s (whole lake)
Lake Huron | Ez = 1.16 cm2/s (whole lake)
Cayuga Lake | Ez = 2.31 cm2/s (whole lake)
Lake Ontario | Ez = 3.47 cm2/s (whole lake)

## Slide 14: Implementing Dispersion in WASP: Exchanges
C1
C2
E12

## Slide 15: Setting Up Dispersion in WASP
1
3
2
4
5
6
Six identical segments. Each 10m x 10m x 10m in size
Purely Dispersive System
Need to set up exchange between each segment:
    Ex = 10-4 m2/sec
C1 = 0.6 mg/L
C2 = C3 = C4 = C5 = C6 = 0.0 mg/L

## Slide 16: Segment Structure Set Up
Use Simple Toxicant Module
Run from
  1/1/2000 00:00 to 7/1/2000 00:00
  Time Step of 0.1 days
  Print Interval of 1 day
6 segments of 10m x 10m x 10m
Model Conservative Toxicant
Bypass Solids
Initial Concentration of 0.6 mg/L in Segment 1

## Slide 17: Segment Tab
Set up 6 Water Segments
1000 m3 each
10 m deep

## Slide 18: Set Up Exchanges

## Slide 19: Set Up Exchanges
Turn on “Surface Water”
Define “Exchange Function” as “Lateral Dispersion”
Define Exchanges from Segment one to Segment two
Define value as 0.0001 m2/sec

## Slide 20: Set Up Exchanges
WASP Structure of Exchanges requires
  E12 = Dispersion Exchange Coefficient [m2/s]
  A12 = Cross-section Dispersion Area [m2]
  L12 = Characteristic Dispersion Length [m]
    typically defined as 0.5*(L1 + L2)
    where L1 and L2 are the lengths of
    segments 1 and 2.
Therefore, Area = 100 m2 and Distance = 10 m

## Slide 21: Set Up Exchanges

## Slide 22: Dispersion Output

## Slide 23
0 5 15 25 35 45 50
600
400
300
200
100
0
500
Distance
Concentration [ug/L]