## Slide 1: Las Virgenes Biosolids Application Study
… a sneak peak at the data

## Slide 2: Biosolids on fire damaged lands
We know biosolids provide exceptional conditions for the recovery of impaired lands
What are the potential impacts to runoff?
We analyzed rainwater runoff from plots with biosolids applied at a burn area

## Slide 3: Woolsey Fire
RANCHO LAS VIRGENES
COMPOST FACILITY

## Slide 5: Three types of biosolids – Block Design
Class A compost | Class b BIOSOLIDS CAKE | Class A pellets (EQ) | control
Compost from LVMWD-Triunfo Sanitation District | Biosolids from LVMWD WWTP (Tapia) | City of Corona WWTP provided by Synagro | Nothing added
< 3”, surface applied 3 treatment plots, approx. 30 ft2/plot | < 3”, surface applied 3 treatment plots, approx. 30 ft2 | < 3”, surface applied 3 treatment plots, approx. 30 ft2 | 3 treatment plots, approx. 30 ft2
3 sampling events: Dec, Jan & March | 3 sampling events | 3 sampling events | 3 sampling events

## Slide 6: Las Virgenes Compost Facility, Calabasas, CA

## Slide 7: Sample Collection and Analysis
We collected samples over 3 rain events in December, January and March (beginning of COVID quarantine)
Volumes recorded in each rain barrel and samples were collected in jars for volatile organic chemicals, semi-volatiles, PCBs, pesticides, metals and wet chemistry.
Samples analyzed by LA City Sanitation laboratories at Hyperion Wastewater Plant

## Slide 8: Rapid revegetation
January 2020
All sets revegetated rapidly with the exception of pelletized
  R to L: A, B, P, C
Pelletized applications had noticeably less growth

## Slide 9: Results Summary
No detectable concentrations of pesticides, volatiles, semi-volatile compounds or PCBs.
Most metals were non-detect especially Lead, Arsenic and Cadmium.
Results were normalized for flow rate to present Mass exported (mass of compound lost to runoff) – achieved by multiplying mass-units/L * volume of runoff captured (L).
Limited number of samples for each treatment type (n~9). Data can be visualized in aggregate (n~36) as quasi-lognormal. Still data is best treated with non-parametric methods (Kaplan-Meier Mean Estimates).
**More samples are advised!

## Slide 10: Observations from Data Analysis
No apparent effect due to sampling event/storm event.
Sample sizes are very limited and some data missing. Non-parametric statistics are recommended.
Visualizations should use lognormal scale, show all results (including non-detects) and outliers
Statistics computed in R-Studio using NADA, EnvStats and other packages after Helsel 2020.

## Slide 11: Total Suspended Solids
A - Compost performs the best, Mass exported also reduced by B compared to Pellets and Control
Pellets consistently increased Mass exported in most compounds/analytes

## Slide 12: Nitrogen as Nitrate

## Slide 13: Ammonia as Nitrogen

## Slide 14: Total Phosphate

## Slide 15: Estimated mean Mass exported – Class A Compost is projected winner
Nitrate | Ammonia | Total phosphate
A and B both seemed to outperform the control | Class A and control were very similar | Significant difference between A and B-C
Class A Compost, 95% UCL mean Mass Nitrate export: 54.48 mg | Class A Compost, 95% UCL mean Mass Ammonia export: 97 mg | Class A Compost, 95% UCL mean Mass Phosphate export: 12.09 mg

## Slide 16
March 2020
May 2020

## Slide 17: Conclusions
Class A compost and Class B cake encourage rapid revegetation of soils in fire ravaged areas.
Impacts to water runoff appear to be indistinguishable from control plots and can be predicted.
More sampling is recommended. The study provides needed science on what compound classes are important in surface water monitoring.
Results overall support application of biosolids to fire damaged sites

## Slide 18: Thank you
Harry Allen, EPA
David Crohn, UCR
Veronica Hurtado, LVMWD
Susan Chang, LA City Sanitation
Greg Kester, CASA
Funding from, WERF