## Slide 1: CENTRAL MARIN SANITATION AGENCY’S ORGANIC WASTE AND POWER DELIVERY PROGRAMs
California Bioresources Alliance Symposium
November 13, 2020

## Slide 2: PRESENTATION OUTLINE
About CMSA and its Organic Waste Program
Food to Energy Program with Marin Sanitary Service
Program Benefits, Metrics, & Cost Information
Power Delivery – Interconnection & Purchase Agreements
What’s Next

## Slide 3: About CMSA and organic waste program

## Slide 4: Central Marin Sanitation Agency - CMSA
Regional Wastewater Agency in San Rafael, Marin County
Serves about 110,000 people and San Quentin State Prison
Joint Powers Agency (JPA) with four satellite collection agencies
Wide range of influent flows: 8 MGD (ADWF) to 121 MGD (PWWF)
Contract services:
  Collection system O&M for two agencies
  Pump station O&M for SQ prison
  Source control for seven local agencies

## Slide 5: Organic Waste to Energy
Organic Waste
Biogas (methane)
Process:
Anaerobic digestion

## Slide 6: Organic Waste to Energy
Anaerobic Digesters
CO2
Biosolids
Electricity for sale to MCE
Beneficial reuse: Landfill ADC and Soil Amendment/Fertilizer
Biogas
Engine/Generator
Food Waste Receiving and Separation at MSS Transfer Station
Organic Waste

## Slide 7: First FOG Load – November 2013

## Slide 8: First Food Waste Load – January 2014

## Slide 9: Food To Energy Program

## Slide 10: Public-Private Partnership
Central Marin Sanitation Agency

## Slide 11: Marin Sanitary Program Details
Focus on Contamination Removal
Customer Enrollment
  Pre-consumer commercial food waste is collected and then transported to the MSS transfer station for processing to remove contamination and then delivered to CMSA.
    250+ commercial food waste producers participate
      Continue adding more participants incrementally
Program outreach
    Kitchen staff training
    Frequent monitoring
    Retraining as-needed

## Slide 12: Food Waste Collection
Notes: Bullet 1 – Public Outreach/Acceptance, raise their rates, Kitchen Staff Training (Continuous/Turnover), Bins Ready, Trucks Pickup and Initial Screening, and Restaurants get a participation sticker.
Bullet Point 2 - Its Important to note that MSS and CMSA Opted for Pre-Consumer Waste, and I do not have a time frame for our two organizations to move away from this model
Continuous Training of Staff/Dedicated Waste Bins and Trucks/Screening Equipment

## Slide 13: Marin Sanitary Equipment
2008 Design Concept
2013 As Built

## Slide 14
CLEAN FEEDSTOCK

## Slide 15: CMSA Organic Waste Facility

## Slide 16: Digestion and Biogas Cleaning
Anaerobic digesters with membrane covers
Biogas H2S Removal

## Slide 17: Biogas cleaning & Cogeneration
Biogas - moisture and siloxane removal
750 kW cogeneration system

## Slide 18: Facility Operations
Receive organic loads between 6:00 am and 12:00 pm
Mix material for 1 hour +/-
Final screenings removal
Slowly feed material to digesters over 18 hours
SCADA Overview Screen of the OWRF
Notes: Ops. Flexibility – Introduce Recycled Water/FOG/Digested Sludge for FW Mixing
Pumps and Piping X-Functional – Redundancy Built-in for the most Part
Fully Automated Process Sequencings – Mixing Would Stop when Initiating a Delivery/Level Indicators to Close FOG Receiving MOV if pit full/Line Flushing Duration/Looks at Dig. Liquid Levels to determine if they can be fed or not

## Slide 19: Metrics, Benefits, & Cost Information

## Slide 20: 2019 Operational Metrics – Feed & Digester Info
Organics | Amount | Loads
Food Waste | 2,447 tons | 348
FOG | 3.36 million gallons | 672
Material | TS - lbs | VS - lbs | %VS
Primary Sludge | 3.67 million | 3.07 million | 36%
TWAS | 3.35 million | 2.80 million | 34%
Organic Slurry | 2.68 million | 2.48 million | 30% (52% max)
 | Alkalinity mg/L | VA mg/l | VA/ALK | PH | HRT days | VSR %
Min | 4,964 | 37.1 | 0.0074 | 7.22 | 33.7 | 56.1
Max | 5,345 | 98.2 | 0.0196 | 7.42 | 60.6 | 71.8
Ave | 5,094 | 57.5 | 0.0113 | 7.31 | 44.3 | 66.2
Digester Health
Digester Feed
Organics Delivered
 | Biogas | Cogeneration
Max month | 316K ft3/day | 22.6 hours/day
Ave month | 277K ft3/day | 17.8 hours/day
Biogas Use

## Slide 21: Program Benefits
A local renewable energy project
Reduces landfilling of food waste; reject material is composted by MSS
  Compliance with SB 1323 – organic waste diversion
Increases CMSA’s energy self sufficiency to align with State renewable energy generation goals
Utilization of existing unused asset capacity – cogeneration system and digesters
CMSA has delivered energy to local utility grid (MCE) since May 2019
Reduces greenhouse gas emissions
Notes: JAF
“Anaerobic Digestion of Food Waste” EBMUD

## Slide 22: Program Revenues and Expenses
Capital Expenses (2013):
  MSS Equipment – $530K
  CMSA OWRF – $2 million
Operational Expenses (2019):
  MSS – $315K for collection, processing, disposal and outreach
  CMSA - $237K for operations, maintenance, administration, and supplies
CMSA Revenues (2019):
  Tipping fees - $155K
  Avoided NG purchasing due to biogas generation - $145K
CMSA Operating Objective: Annual Revenues > Expenses

## Slide 23: Power Delivery

## Slide 24: Power Delivery - Interconnection
Need approval from local electrical utility – PG&E
Utility performs electrical system evaluations
CMSA needed to:
  Design, install, and test protective relays
  Pay for utility review of design work
  Test and possibly replace a ground detection bank
  Install a revenue meter
Permission to Operate received on 3/14/19
Notes: JAF
“Anaerobic Digestion of Food Waste” EBMUD

## Slide 25: Power Delivery – Power Sale Agreement
Two electrical utilities serve CMSA – PG&E and MCE
Identified and evaluated several Feed-in-Tariffs from both utilities
Selected Small Generator Power Purchase Agreement with MCE
  Minimal administration, no power scheduling, buy what we deliver – no delivery commitments
Purchase price is $0.105 kWh
Attained the Commercial Operations Date on 4/26/19
First delivered power on May 29
Power export
Notes: JAF
“Anaerobic Digestion of Food Waste” EBMUD

## Slide 26: What’s Next

## Slide 27: Power Delivery – New Cogen System
Installing a new higher capacity cogeneration system and use the existing system as a back-up
Prepurchased a 995 kW high efficiency system for $1.6 million - Jenbacher
Awarded construction contract for the system installation last Tuesday - $3.6 million
Online in late 2021
Applied for and received a new PG&E Interconnection Agreement. System improvements being designed.
New PPA with MCE in development, at a lower purchase price - $0.08 kWh.
Notes: JAF
“Anaerobic Digestion of Food Waste” EBMUD

## Slide 28: Digester Pilot Study
Purchased a pilot digester system, made repairs, added equipment, and got it ready for operation
Worked with a consultant technical advisory group to prepare a study plan
Study has been running for over 12 months
Objective: Determine if there is an organic waste loading limit, to prevent a full-scale digester upset.
Started pilot at 30% loading rate and currently running pilot at 60%.
Test digester system as of 7/12
Notes: JAF
“Anaerobic Digestion of Food Waste” EBMUD

## Slide 29: Questions ?