## Slide 1: ZERO ORGANICS TO LANDFILL Hilary Gans CBA 11/13/20 hgans@rethinkwaste.org
Notes: Do you recognize these logos where have you seen them before?

## Slide 2: SBWMA Environmental Goals: “Triple-Zero”
Zero
Organics to Landfill
1
Zero Recyclables to Landfill
2
Zero
Net GHG in Operations
3

## Slide 3: California Mandates to Reduce Methane from Organics
New Gen. Legislative Mandates
Reduce waste 75% by 2025 (vs. 2014 levels)
organics to landfill = methane/GHGs
SBWMA currently at 50%
AB 32-Global Warming Act (2006)
AB 341-Mandatory Commercial Recycling Act (2011)
AB 1594-Yard Trimmings & ADC LF Limits Act (2014)
AB 1826-Mandatory Organics Recycling Act (2014)
SB 1383-Short-Lived Climate Pollutants Act (2016)
Organics-Specific Diversion Laws:

## Slide 4: Solid Waste Sector Goals & Gaps
75% Goal
Note: 10% diversion-boost from “Single Stream” recycling, making recycling convenient for users
25% Diversion Gap

## Slide 5: Organics: Largest % of Waste Stream
Residential Waste
Commercial/MFD Waste
Organics/food waste is largest single category of landfilled material for both Commercial/MFD & Residential

## Slide 6: Barriers to Increasing Organics AD
Cost effective preprocessing of waste
Production of a clean organic stream from MSW
Cost efficient AD of organics (compared to compost)
Regulatory uncertainty (Air & Water Board)
Complexity of energy utilization and off-take

## Slide 7: MSW Preprocessing & Contamination

## Slide 8
Lack of composting capacity
Transporting & composting food waste $75-$100 ton
Composting food waste is problematic
No clear alternatives to composting (WWTP AD is viable but not a proven pathway)
Diverting Organics is Costly

## Slide 9: O2E Process and Partnerships
Organic pre-processing at Shoreway
SVCW, Redwood City
Organic Digestion & energy production at Partnering WWTP
CMSA, San Rafael
EBMUD, Oakland
SSFWQCP, SSF
Notes: What to do with the Organic Fraction of the Solid Waste -

## Slide 10: Organics to Energy (O2E) Process
Organic Slurry
Extracting
OFMSW
MSW
Sorting Organics
MSW/SSO
Collecting
SSO/MSW
Anaergia OREX Press - Extracting Organics

## Slide 11: O2E Pilot Equipment at Shoreway
Storage Tanks
Truck Load Out
Shredder
Polisher
OREX

## Slide 12: O2E Pilot Expense & Source of Funds
($5,000,000) | Anaergia Equipment Installed Cost
$ 1,200,000 | CalRecycle – Repurposed Orex Press
$ 1,800,000 | CalRecycle – Polisher Grant
$ 1,000,000 | San Mateo County Grant
$ 1,000,000 | Total SBWMA CapEx Cost

## Slide 13: Organics-to-Energy (O2E) ProJet Phasing
Phase 1: O2E Pilot
Validate full 02E system diversion
Validate WWTP AD partnership
Phase 2: Full O2E w/ MSW Sorting)
Eliminate Organics to landfill
Eliminate Recyclables to landfill
Reduce GHG emissions from LF + trucking
Phase 3 (option): CNG / Bio-CNG
Convert Collection Fleet to CNG
Replace diesel with BioCNG

## Slide 14: Full-O2E w/ MSW Sort System
MSW Presort In-feed
400 TPD
Organic Slurry Output to WWTP AD 150TPD/12%TS
OFMSW
In-feed
100TPD/25%TS
25% capture
75% capture

## Slide 15: O2E Benefits (Diversion, Green Energy, and GHG)
Electricity
Production
BioCNG
Production
Pilot
Full Scale

## Slide 16: Benefits of Solid Waste/WWTP Partnership
Reduced Methane GHG emissions
Recovery of green-energy from organics
Ratepayer benefits (trash and WWTP overlap)
Demonstrates public agency value & coordination
Maximize utilization of infrastructure and expertise
Potential BioCNG fleet fueling opportunities
Demonstrates success for future projects/grant

## Slide 17: The O2E project represents the single greatest action that the RethinkWaste can take to mitigate GHG & climate change

## Slide 18
SUPPORT SLIDES

## Slide 19
Current: Comm./MFD w/Organic Service = Approx. 20%
Current: Comm. Organic (SSO) Lifts = 7%
Double Organics Lifts to 14% = Increase of $2.5M/year in Collection Costs
Adding Commercial Organics Collection is Expensive
(And Does Not Solve the Contamination issue)

## Slide 20: O2E Full-System Projected Overall SBWMA Diversion
Projected Diversion – 66%
O2E Project will Increase SBWMA Diversion 16%

## Slide 21: O2E Pilot Project - Financial Summary
O2E Pilot Cost Category (Based on ~20,000 tons/year) | $/Ton | Total $/Yr.
CAPEX (Budget amount of $2.25M) | 11.54 | 225,000
OPEX | 10.95 | 213,504
Organic Slurry to WWTP (T&D) | 52.50 | 1,023,750
Residual Disposal to Landfill (T&D) | 14.43 | 281,434
Total Cost of O2E Pilot | $89.42 | $1,743,688
Organic to Compost Cost | $/Ton | Total $/Yr.
Current Cost of Transport & Compost | $69.20 | $1,349,400

## Slide 22: SBWMA Technology Partner - Anaergia
Integrated Solutions Provider
Processing Waste
Municipal Solid Waste
Collected Food Waste
Wastewater Biosolids
Clean Water
Renewable Gas
Agricultural Waste
Fertilizer
Renewable Power
Recyclables

## Slide 23
Anaergia Major Projects
Limassol, Cyprus
Processes 140,000 TPY of MSW using OREX and a suite of Anaergia technologies to produce biogas, recyclables, and RDF to achieve 89% recovery
Operational: September 2017
Toronto Canada
Processes 70,000 TPY of OFMSW using OREX at Recology
Operational in April, 2019
Goa, India
Processes 36,000 TPY of MSW using OREX and a digester to produce electricity, biogas, and refuse derived fuel (RDF) achieving a 94% recovery.
Operational: March 2016
Cardiff, UK
Processes 42,000 TPY of SSO food waste using OREX
Operational: December 2016
Cape Town, South Africa
Processes 140,000 TPY of MSW using OREX to produce wet fraction for AD and bio-methane.
Operational: March 2017
Singapore
Processes 35,000 TPY of SSO with 25% contamination using OREX and a digester and generating 2MW of power.
Operational: November 2016

## Slide 25: O2E Full-Project Financial Summary
O2E Full-Project Cost Category (Based on ~200,000 tons/year) | $/Ton | Total $/Yr.
CAPEX Depreciation (Financing not Included) | 8.24 | 1,500,000
OPEX (Sort System Operations) | 9.75 | 1,774,803
Organic Slurry to WWTP (T&D) | 8.40 | 1,528,800
Residual Disposal to Landfill (T&D) | 48.24 | 8,779,680
Total Cost of O2E | $74.63 | $13,583,283
Business As Usual Cost Comparison | $/Ton | Total $/Yr.
Disposal Cost (Landfill, Compost & Transport) | 72.00 | 13,104,000
Additional Organics Collection Cost | 13.74 | 2,500,000
Total BAU Cost (without O2E) | $85.74 | $15,604,000

## Slide 26: O2E Implementation Schedule