## Slide 1: Chapter 5
Writing the Report
Notes: Chapter 5: Writing and Delivering the Report
Lead Dust Sampling Technician Training Course
5-<number>

## Slide 2: Objectives
List the items that make up a complete lead dust clearance test report.
Make the report easy for the client to understand.
Notes: Chapter 5: Writing and Delivering the Report
Lead Dust Sampling Technician Training Course
5-<number>
At the end of the chapter, students will be able to:
  List the key contents of a complete lead dust clearance test report
  Describe ways to make the report easy to read
  Respond appropriately to questions that clients may ask upon receiving their report

## Slide 3: Contents of Report – EPA RRP
Cover Page
Summary of Sampling Results
Visual Inspection Results
Laboratory Analytical Results
Renovate Right Pamphlet
  (Appendix B)
Notes: Chapter 5: Writing and Delivering the Report
Lead Dust Sampling Technician Training Course
5-<number>
These are the six elements of the Lead Dust Clearance Test Report.
Blank forms that can be used for the Cover Page, Summary of Sampling Results, and Visual Inspection Results are provided in Appendix B of this course.
A copy of the Renovate Right: Important Lead Hazard Information for Families, Child Care Providers and Schools pamphlet is also included in Appendix B.

## Slide 4: Contents of Report – HUD LSHR
Address of property and if multifamily, specific units and common areas affected
Date of clearance exam
Name, address and signature of person performing clearance including certification number
Visual inspection results
Notes: Because HUD has more extensive visual inspections requirements, than does the EPA rule, HUD requires more information regarding the details of a lead dust clearance test report.

## Slide 5: Contents of Report – HUD LSHR (Cont.)
Dust sampling results
Name and address of each laboratory that analyzed samples
Start and completion dates of work performed
Detailed written description of methods used during work and specific, detailed locations where work occurred
If soil hazards are corrected, description of location.
Notes: Because HUD has more extensive visual inspections requirements, than does the EPA rule, HUD requires more information regarding the details of a lead dust clearance test report.

## Slide 6: Activity: Writing the Report
Refer to Attachment 5-A and 5-B
Review the blank and completed Lead Dust Clearance reports
Notes: Chapter 5: Writing and Delivering the Report
Lead Dust Sampling Technician Training Course
5-<number>

## Slide 7: Summary
The items that make up a complete lead dust clearance test report
How to make a report easy for a client to understand
Notes: Chapter 5: Writing and Delivering the Report
Lead Dust Sampling Technician Training Course
5-<number>