## Slide 1: Chapter 6
Putting the Skills Together
Notes: Chapter 6: Putting the Skills Together
Lead Dust Sampling Technician Training Course
6-<number>

## Slide 2: Objectives
Practice the skills taught in the class:
  Choosing appropriate sampling locations
  Taking lead dust samples
  Interpreting Results
Notes: This chapter will outline the steps a lead dust sampling technician must take from start to finish when conducting an examination. This chapter includes five activities to help practice implementing the protocols.
By the end of this chapter, students will be able to demonstrate that they can:
  Choose appropriate sampling locations
  Take lead dust samples
  Interpret Results
6-<number>
Lead Dust Sampling Technician Training Course
Chapter 6: Putting the Skills Together

## Slide 3: Activity 1: Where To Take Samples
You are now going to practice sampling area strategies.
Your instructor will provide you with a hypothetical renovation scenario and diagram.
Read the scenario and mark the location(s) of where you think dust wipe samples should be taken.

## Slide 4: Remember…
Be strategic about laying out sampling area to capture areas were the highest dust generating tasks occurred during the job.
Refer to the Field Guide or Chapter 3 to determine the appropriate places to take your samples.

## Slide 5: Activity 2: Dust Wipe Sampling
You are now going to practice taking dust wipe samples again.
Each individual must demonstrate proficiency.
Follow your instructor’s directions for taking samples.
Notes: Activity 2: Now that the sampling locations have been determined, you will take samples on a variety of surfaces – windowsills, troughs, and floors.
Chapter 6: Putting the Skills Together
Lead Dust Sampling Technician Training Course
6-<number>

## Slide 6: Activity 3: Interpreting the Results
Analyze the results
  Your instructor will provide you with laboratory results to interpret.
  Use EPA lead dust clearance standards for guidance:
    Floors: < 10 µg/ft2
    Interior window sills: < 100 µg/ft2
    Window troughs: < 400 µg/ft2
Notes: Results and Report Writing
When analyzing the data, follow the guidelines provided in Chapter 4.
Use the EPA/HUD lead dust clearance standards when evaluating sample results.
6-<number>
Lead Dust Sampling Technician Training Course
Chapter 6: Putting the Skills Together