## Slide 1
Chapter 1
Introduction
Notes: Welcome to the Lead Dust Sampling Technician Training Course.

## Slide 2: Course Objectives
Understand what a lead-dust clearance test is.
Identify steps in lead-dust clearance testing.
Learn how to:
  Conduct a visual inspection
  Collect lead dust samples
  Interpret results
  Write a report
  Explain the results to the client
Notes: The EPA has provided this model curriculum to teach individuals how to conduct lead dust clearance testing after renovation activities.
Lead dust clearance testing is often performed to find out whether lead dust remains after renovation, repair, or painting. It is required by HUD’s LSHR regulations for most renovations. By the end of the course, students will be able to perform the actions listed above.

## Slide 3: Overview of Student Materials
Student Manual
Attachments
Appendices
Lead Dust Sampling Technician Field Guide
Notes: The student materials include a student manual, attachments, appendices, and a copy of the Lead Dust Sampling Technician Field Guide.
  The student manual contains copies of the slides that are used by the instructor during the course.
  The attachments and appendices provide important summaries, checklists, tables, and tools you can use.
  The Lead Dust Sampling Technician Field Guide outlines key points and procedures in one easy-to-read reference tool that can be taken along on the job.

## Slide 4: Health Risks of Lead
In children:
  Damage to the brain and central nervous system; can cause developmental and behavioral problems.
In pregnant women:
    Damage to the fetus
In workers:
  Elevated blood pressure
  Loss of sex drive and/or capability
  Physical fatigue
Notes: Children under 6 are most at risk from small amounts of lead.
Children are at a greater risk than adults. During normal and frequent playing or hand-to-mouth activity, children may swallow or inhale lead dust from their hands, toys, food, or other objects.
In children, lead may cause:
  Nervous system and kidney damage
  Decreased intelligence, attention deficit disorder, and learning disabilities
  Speech, language, and behavioral problems
Among adults, pregnant women are especially at risk from exposure to lead.
Lead is passed from the mother to the fetus and can cause:
  Miscarriage
  Premature birth
  Brain damage
  Low birth weight
Health effects of lead in adults include:
  Elevated blood pressure
  Reproductive problems in men and women
  Digestive problems
  Nerve disorders
  Memory and concentration problems
  Sexual disorders
  Muscle or joint pain

## Slide 5: Why Are Dust and Debris a Problem?
Renovations that disturb lead-based paint create dust and debris.
Very small amounts of lead dust can poison children.
Adults can swallow or breathe lead dust during work activities.
Workers can bring lead dust home and poison their families.
Notes: Dust and debris from renovation, repair, and painting jobs in pre-1978 housing and child-occupied facilities may contain lead.
Pre-1978 paint may contain lead.
Common renovation activities like sanding, scraping, cutting, and demolition can create hazardous lead dust and chips by disturbing lead-based paint.
Some tasks, such as power sanding, open flame burning, and the use of heat guns above 1100 degrees Fahrenheit, create large amounts of extremely fine lead dust that is very difficult to clean up.
Small amounts of lead dust can poison children and adults.
A tiny amount of lead can be extremely harmful.
Lead dust particles are often so small that you cannot see them, yet you can breathe or swallow them. These smaller, inhaled or swallowed lead dust particles are more easily absorbed by the body than larger particles, and can therefore more easily cause poisoning.
Lead dust may be breathed or swallowed by children, residents, and workers.
Through normal hand-to-mouth activities, children may swallow or inhale lead dust on their hands, toys, food, or other objects. Children may also ingest paint chips.
Adults can swallow or breathe lead dust during work activities.
  When workers perform activities such as scraping and sanding by hand, or use a power sander or grinding tool, dust is created. The dust goes into the air that they breathe.
  If workers eat, drink, smoke, or put anything into their mouths without washing up first, they may swallow the lead dust present.

## Slide 6: Regulations Addressing Lead Hazards in Housing
To address the issue of lead hazards in housing, EPA and HUD have issued several regulations.
EPA currently oversees the training and certification of abatement contractors, inspectors, and risk assessors.
HUD’s Lead Safe Housing Rule (LSHR) addresses lead hazards in Federally owned and assisted housing.
In April 2008, EPA issued the Renovation Repair and Painting (RRP) Rule to address lead hazards created during renovation.

## Slide 7: Overview of the Lead Hazard Evaluation Courses
Lead Dust Sampling Technician
Lead-Based Paint Inspector
Risk Assessor
  All three disciplines can conduct dust clearance testing after an RRP project
Notes: There are three courses for professionals who wish to be certified to conduct evaluations for lead dust, lead hazards and/or lead-based paint:
  Lead Dust Sampling Technician: This 8-hour training course teaches you how to become a lead dust sampling technician. You will learn how to conduct a visual inspection, collect dust wipe samples, interpret results, and write a lead dust clearance test report.
  Lead-Based Paint Inspector: To become a certified lead-based paint inspector, you must take a 24-hour training course. In the lead-based paint inspector course, you will learn the skills and protocols for conducting a paint inspection. A lead-based paint inspection is a surface-by-surface investigation to locate all lead-based paint on a property. We will talk more about what a paint inspection is in the next chapter.
  Risk Assessor: To become a certified risk assessor, you must successfully complete a lead-based paint inspector course plus an additional 16-hour risk assessor course. In the risk assessor course, you will learn the skills and protocols necessary for conducting risk assessments. A risk assessment is an on-site investigation to identify all lead-based paint hazards on a property.
Today you are taking the LDST Training Course.
Refer to Attachment 1-A: Comparing Lead Evaluation Professionals for additional information.

## Slide 8: Lead Dust Sampling Technician
EPA’s RRP rule also established the lead dust sampling technician discipline.
To work as a dust sampling technician, an individual must successfully complete this training course. The course completion certificate will serve as your certification.
Dust sampling technicians are used in both EPA’s and HUD’s regulations.

## Slide 9: A Lead Dust Sampling Technician Can...
Perform post-renovation lead dust clearance testing under EPA’s RRP Rule
Perform a clearance examination after hazard reduction or maintenance activities in most properties covered by HUD’s LSHR
Is Not Allowed To...
Perform clearance after an abatement
Sample paint for lead content
Sample soil for lead
Notes: A lead dust sampling technician can perform lead dust clearance testing, but not if associated with an abatement.
The purpose of lead dust clearance testing after renovation, repair, or painting activities that disturb lead-based paint is to determine if a work area is safe for re-occupancy. These activities can create lead dust, so proper cleanup is critical.
While lead dust sampling technicians can conduct post-renovation lead dust clearance testing, they are not allowed to conduct post-abatement clearance. Clearance after abatement must be done by a certified risk assessor or a lead-based paint inspector.
Abatements are projects designed to permanently remove or eliminate lead-based paint and lead-based paint hazards.
Abatement does not include renovation, remodeling, landscaping, or other activities, when such activities are not designed to permanently eliminate lead-based paint hazards, but, instead, are designed to repair, restore, or remodel a given structure or dwelling, even though these activities may incidentally result in a reduction or elimination of lead-based paint hazards.
So, if a renovation job involves abatement, the lead dust sampling technician cannot perform lead dust clearance testing on the abatement part of the job. Make sure you understand what type of work was done before conducting lead dust clearance testing.
In addition, a lead dust sampling technician is not trained to test paint for lead content. Paint sampling must be done by a lead-based paint inspector or risk assessor.
Finally, a lead dust sampling technician is not trained to sample soil. Soil sampling must be done by a certified lead-based paint inspector or risk assessor.

## Slide 10: EPA’s RRP Rule
Common renovation activities like sanding, cutting, and demolition can create hazardous lead dust and chips by disturbing lead-based paint.
On April 22, 2008 EPA issued a rule requiring the use of lead-safe practices and other actions aimed at preventing lead poisoning.
Beginning on April 22, 2010, all contractors performing renovation and all dust sampling technicians must be trained and certified.
Notes: Beginning April 22, 2010, contractors performing RRP projects that disturb lead-based paint in homes, child care facilities, and schools built before 1978 must be certified and must follow specific work practices to prevent lead contamination.

## Slide 11: EPA’s RRP Rule – (cont.)
Upon completion of renovation activity, the RRP Rule requires either:
  cleaning verification by a certified renovator, or
  lead dust clearance testing by a certified LDST, lead-based paint inspector, or risk assessor
“Cleaning verification” need not be done if both lead dust clearance testing and achieving clearance is required by:
  the contract between the renovator and the property owner, or
  another Federal, State, or local law
Notes: The cleaning verification process involves a visual inspection of the work area, followed by wiping of the windowsills, floors, and countertops with wet disposable cleaning cloths and comparing the wipes to a cleaning verification card.
Cleaning verification must be performed by a certified renovator; it cannot be done by the lead dust sampling technician and sampling technicians are not allowed to perform clearance on abatement projects or on abatement parts of renovation projects.
See Appendix A for a portion of the EPA RRP final rule.

## Slide 12: EPA’s RRP Rule – (cont.)
You must be a certified LDST to perform post-renovation clearance testing under EPA’s RRP Rule.
Certified LDSTs must complete a refresher course within 5 years of their previous certification.
Successful completion of this course completes the re-certification process.
You will be certified by either EPA, or if they are an authorized program, the State, Tribe, or Territory in which you work.
Notes: To conduct a post-renovation clearance examination, the individual must be a certified lead dust sampling technician, lead-based paint inspector, or risk assessor.
EPA LDST certification allows the certified individual to perform post-renovation lead dust clearance testing in residential housing and child-occupied facilities. Certified lead dust sampling technicians cannot conduct post-abatement clearance testing.
When going to a worksite, lead dust sampling technicians must have a copy of their initial course completion certificate and most recent refresher training course completion certificate.

## Slide 13: EPA’s RRP Rule – (cont.)
Before conducting dust clearance sampling after a renovation, a visual inspection of the work area for dust and debris is required.
Results of dust clearance testing must be interpreted according to the EPA/HUD clearance standards and provided to the client.
All surfaces represented by a failed clearance test must be re-cleaned and re-tested until the clearance level is met.
Notes: More details on all these topics are discussed later in the course.

## Slide 14: HUD’s Lead Safe Housing Rule – (LSHR)
HUD requires clearance testing on all but very small renovation or maintenance jobs.
Clearance must be performed by a clearance examiner who is independent of those performing work (third party).
This clearance must be performed by either a certified lead-based paint inspector, risk assessor, or sampling technician.
HUD requires a visual inspection (assessment), dust sampling, laboratory analysis, and submission of a clearance report.
Notes: HUD’s LSHR requires that lead hazards be corrected in target housing receiving Federal housing assistance or being sold. It also requires clearance dust sampling as a routine part of every such activity, unless very small amounts of paint are disturbed.

## Slide 15: HUD’s LSHR – (cont.)
HUD clearance generally covers an entire dwelling unit, common areas, and exteriors.
Worksite-only clearance is permitted on certain renovation or maintenance jobs.
  For ongoing lead-based paint maintenance
  Rehabilitation assistance up to and including $5,000 per unit
Clearance report must include specifics of property, results of visual inspection, laboratory information, dates, written description of work performed, and dust testing results.
Notes: Clearance must be on the entire unit unless the worksite has been properly contained or the LSHR specifically permits worksite-only clearance. The LSHR permits worksite-only clearance for units receiving rehabilitation assistance up to and including $5,000 and for ongoing lead-based paint maintenance activities.
Sampling requirements will be discussed in later chapters.

## Slide 16: HUD’s LSHR – (cont.)
Use EPA/HUD clearance standards to interpret dust sampling results.
HUD requires that all surfaces represented by a failed clearance test be re-cleaned and re-tested until the clearance level is met.
If the work area fails the visual inspection, the sampling technician must stop and require the renovator to re-clean.
The sampling technician must then re-inspect before dust testing.
Notes: Details on these topics are provided later in the course.