## Slide 1: Module 1: Why Should I be Concerned about Lead Paint?
October 2011
1-<number>
Overview
What is lead-based paint?
What health risks and health effects are related to lead exposure?
Why is lead-contaminated dust a problem?
Notes: Lead Safety for Renovation, Repair, and Painting
1-<number>
October 2011
Upon completion of this module, you will be able to explain:
What lead-based paint is and why it is a problem for renovators.
The health risks of lead to children and adults.
Why we are concerned with lead-contaminated dust.

## Slide 2: What Is Lead-Based Paint?
October 2011
1-<number>
Federal standards define lead-based paint as:
  Any paint or surface coatings that contain lead equal to or in excess of 1.0 milligram per square centimeter or more than 0.5 percent by weight.
  Some states and localities regulate paint with lower concentrations of lead.
  It is the primary source of lead-contaminated dust in housing.
Why was lead used in paint?
  Lead was added for color and durability.
Lead-based paint was banned in 1978.
Notes: Lead Safety for Renovation, Repair, and Painting
1-<number>
October 2011
Federal standards define lead-based paint.
  Lead-based paint is any paint or surface coatings that contain lead equal to or in excess of 1.0 milligram per square centimeter or more than 0.5 percent by weight.
  Paint with concentrations of lead lower than the definition above can still cause health problems. Even paint with a small amount of lead can account for a lot of lead in airborne or settled dust.
  Information on how to determine if a property contains lead-based paint is provided in Module 3.
Some states and localities regulate paint with lower concentrations of lead.
  You should check with your state and local health departments to see if they have requirements that are more stringent than the Federal requirements.
Why was lead added to paint?
  Lead was added for color and durability.
  Lead was also added to some other surface coatings, such as varnishes and stains.
Lead-based paint was banned from residential use in 1978
  In 1978, the Consumer Products Safety Commission banned the sale of lead-based paint for residential use. In practice, this means that homes built in 1978 could still have used lead-based paint, because existing supplies of paint containing lead would still have been available.
  This is why the year of construction is such an important consideration.

## Slide 3: Health Risks of Lead
October 2011
1-<number>
Very hazardous to children.
  Damages the brain and central nervous system; can cause decreased intelligence, reading and learning difficulties, behavioral problems, and hyperactivity.
  Damage can be irreversible, affecting children throughout their lives.
Hazardous to pregnant women.
  Damage to the fetus.
Also hazardous to workers and other adults.
  High blood pressure.
  Loss of sex drive and/or capability.
  Physical fatigue.
Lead exposure causes permanent damage.
Notes: Lead Safety for Renovation, Repair, and Painting
1-<number>
October 2011
Children under six are most at risk from small amounts of lead.
  Children are at a greater risk than adults because their bodies are developing. During normal and frequent playing or hand-to-mouth activity, children may swallow or inhale dust from their hands, toys, food or other objects.
  In children, lead can cause:
    Nervous system and kidney damage.
    Decreased intelligence, attention deficit disorder, and learning disabilities.
    Speech, language, and behavior problems.
Among adults, pregnant women are especially at risk from exposure to lead.
  Lead is passed from the mother to the fetus and can cause:
    Miscarriages
    Premature births
    Brain damage
    Low birth weight
Health effects of lead in adults include:
  High blood pressure.
  Fertility problems in men and women.
  Digestive problems.
  Nerve disorders.
  Memory and concentration problems.
  Sexual disorders.
  Muscle or joint pain.

## Slide 4: Symptoms Of Lead Poisoning are Not Always Obvious
October 2011
1-<number>
  Symptoms are easily misinterpreted by medical personnel, thus delaying effective treatment and increasing the likelihood of permanent physical and mental damage.
  Only sure way to determine lead poisoning is to take a blood lead level (BLL) test.
Notes: Lead Safety for Renovation, Repair, and Painting
1-<number>
October 2011
Lead poisoning does not always have obvious symptoms.
The symptoms of lead poisoning are often non-specific, and are frequently attributed to other causes.
Specific symptoms that people with lead exposure sometimes complain of include:
  Headache
  Stomach ache
  Irritability
  Fatigue
  Loss of appetite
  Joint and/or muscle pain
Because many symptoms are non-specific or similar to flu symptoms, parents may not be alerted to get immediate medical attention for their children. This is critical for young children. The longer a young child stays untreated, the higher the risk of permanent brain damage.
Workers with an occupational exposure to lead need to inform their doctors in order to give them all the background needed for an adequate evaluation of symptoms as possibly related to lead exposure.
The best way to determine if lead is present in the body is by testing blood.
The amount of lead in blood is measured in micrograms per deciliter (g/dl) of the blood, a very small unit of measurement. A microgram is one millionth of a gram. That is like one penny out of $10,000. For reference, a standard size paper clip weighs about one gram, or one million times more than a microgram. A microgram is a very small amount of lead. Remember how small this amount of lead is as it applies to dust cleanup when we get to Module 4: Contain Dust During Work, Module 5: During the Work, and Module 6: Cleaning Activities and Checking Your Work.

## Slide 5: Why are Dust and Debris a Problem?
October 2011
1-<number>
Renovation activities that disturb lead-based paint create dust and debris. Debris becomes dust.
Lead-contaminated dust is poisonous.
Very small amounts of lead-contaminated dust can poison children and adults.
  Children swallow dust during ordinary play activities.
  Adults swallow or breathe dust during work activities.
Workers can bring lead-contaminated dust home and poison their families.
Notes: Lead Safety for Renovation, Repair, and Painting
1-<number>
October 2011
Dust and debris from renovation, repair, and painting jobs in pre-1978
housing and child-occupied facilities may contain lead.
Pre-1978 paint may contain lead.
Renovation, repair and painting jobs disturb paint that may contain lead. Any activity involving surface preparation, such as hand-scraping, power sanding, the use of heat guns above 1100O Fahrenheit, and open flame burning, can generate lead dust. More complicated tasks such as removing building components and demolishing walls also can create a lot of dust.
Small amounts of lead-contaminated dust can poison children and adults.
A tiny amount of lead can be extremely harmful.
Leaded-dust particles are often so small that you cannot see them, yet you can breathe or swallow them. These smaller, inhaled or swallowed dust particles are more easily absorbed by the body than larger particles, and can therefore more easily cause poisoning.
Leaded dust may be breathed or swallowed by children, residents and workers.
Through normal hand-to-mouth activities, children may swallow or inhale dust on their hands, toys, food, or other objects. Children may also ingest paint chips.
Adults can swallow or breathe dust during work activities.
  When workers perform activities such as scraping and sanding by hand, or use a power sander or grinding tool, dust is created. The dust goes into the air that they breathe.
  If workers eat, drink, smoke or put anything into their mouths without washing up first, they may swallow the leaded dust present.

## Slide 6: A Little Dust Goes a Long Way
October 2011
1-<number>
You can’t see it.
It’s hard to sweep up.
And, it travels.
One gram of lead-based paint can contaminate a large area!
Notes: Lead Safety for Renovation, Repair, and Painting
1-<number>
October 2011
A little dust goes a long way.
You can’t see it. Even a floor that looks clean can have leaded dust on it. Only a laboratory test can tell you for sure if an area is contaminated with lead.
It’s hard to sweep up. Normal cleaning methods will not pick up all the dust in a work area. Sweeping is not enough. You need to use water, detergent and a HEPA vacuum to clean up dust effectively.
It travels. Once dust is released, it is easily tracked around, inside and outside the work area. And, an exterior painting job can contaminate the inside of a home as the dust, chips and leaded soil are tracked inside.
Later in this course we will discuss in detail the EPA and HUD dust-lead hazard and clearance standards. The limits are included here to reinforce the idea that a very small amount of lead can cause health problems. These numbers represent the amount of lead measured in micrograms (1 millionth of a gram) that is allowed in an area one foot wide and one foot long (one square foot). More than this amount of lead in the specified areas is hazardous.
EPA & HUD use these standards when clearance is performed:
  Floors 10 g/ft2
  Interior window sills 100 g/ft2
  Window troughs 400 g/ft2
  NOTE: States and localities may enforce lower standards.

## Slide 7
October 2011
1-<number>
Video Clip of a Contractor Who Poisoned His Own Kids
Notes: Lead Safety for Renovation, Repair, and Painting
1-<number>
October 2011
Contractor discusses how lead safe work practices could have protected his kids from becoming lead poisoned.
The video shown at this point in the course is of Kevin Sheehan, a lead contractor, who discusses how he poisoned his family while working on older houses which contained lead-based paint. Kevin discusses the need for lead safety precautions during renovation work, shares the lessons he has learned, and reveals what can be done to keep people safe during work in older homes with lead-based paint.

## Slide 8
October 2011
1-<number>
Video Clip of Parent of a Child Poisoned by Renovation
Notes: Lead Safety for Renovation, Repair, and Painting
1-<number>
October 2011
Parent Discusses Child Poisoned by Renovation Undergoing Treatment.
The video shown at this point in the course shows Maurci Jackson, a parent whose child became lead poisoned, discussing how hard it was to watch her daughter undergo “chelation” treatments to remove lead from her body. Maurci shares her fears about her child’s future health after being lead poisoned and her frustration that lead poisoning is completely preventable if those who disturb lead-based paint would just considered the consequences of working with lead improperly. She emphasizes the need for lead safety precautions and planning to prevent lead poisoning.
Note: Chelation treatment is a series of medical procedures that remove lead from the body.

## Slide 9: Now You Know…
October 2011
1-<number>
What lead-based paint is and the adverse health effects of lead.
Dust is the problem.
Lead poisoning is hard to spot and the effects can be permanent.
Kids are most at risk for lead poisoning.
Lead poisoning is preventable.
Notes: Lead Safety for Renovation, Repair, and Painting
1-<number>
October 2011